## Slide 1: Nutating Disk
By: John Adrian m. Castillo

## Slide 2: What is nutating disk?

## Slide 3: Nutating disk
Nutating disk flow meters are one of the most common type of positive displacement flow meter.
This type of flow meter is normally used for water service, such as raw water supply and evaporator feed.

## Slide 4: Design/construction

## Slide 5
It consists of a precision machined chamber, a center ball, movable disc, and counter mechanism. The disc is integral to the ball/sphere mounted inside the chamber. A small pin is fastened to the ball to convert nutating motion/ eccentric spinning motion of the ball into rotary motion of the shaft. The disc is pivoted at the geometric center, and it is allowed to nutate or wobble in a specially designed chamber. The controlled clearance between the disc and chamber ensures the proper sealing and minimum leakage.

## Slide 7: How does it work?

## Slide 8
The disc divides the chamber into two equal volume. Water enters at the left side of the eccentrically mounted disc. The liquid pressure sets the disc in motion, results in the quantity of liquid that enters left side of the chamber will be rolled out through the outlet. When the disc and ball wobble it generate a cone with the apex at geometric center, this motion is getting translated into a rotary motion of shaft by the pin fastened to the ball. The movement of the disc is then transmitted by the cam and gear train to the totalizer or pulse transmitter. Each complete cycle of nutation of the disc will be counted by the counter mechanism which can be directly calibrated in terms of volume of liquid received or discharged. Each revolution of disc indicates the passage of fixed volume of fluid.

## Slide 9: Advantages/disadvantages

## Slide 10: Advantages
Relatively low cost
Less affected by the velocity profile in downstream and upstream.
The nutating disk are durable, minimum maintenance.
High accuracy, repeatability. (Accuracy is about +-1%)
Low pressure drop
May be constructed from a variety of materials.

## Slide 11: Disadvantages
Performance may affected by suspended solid particle.
It is limited to pipe size and capacity.
Only clean fluid can be measured.
Accuracy is affected by the viscosity of fluid flow through them.

## Slide 12: Rotating impeller

## Slide 13: What is rotating impeller?

## Slide 14: Rotating impeller
Nutating disk flow meters are one of the most common type of positive displacement flow meter.
This type of flow meter is normally used for water service, such as raw water supply and evaporator feed.

## Slide 15: Design/construction

## Slide 16: How does it work?

## Slide 17: Advantages/disadvantages